Illustra, the IP camera product line for Security Products, a division of Building Technologies & Solutions for Johnson Controls, is a leading manufacturer and designer of video surveillance products. Security and other industries require a full line-up of cyber secure, high-definition video devices that provide superior low-light, wide dynamic range, low network latency, multiple codecs and streams. The Pro, Flex and Essential family of Illustra IP cameras include PTZ and Fisheye devices, as well as a variety of different form-factor cameras such as Mini-Dome, Bullet, Box and Micro.

For additional information, please contact: Tyco Security Products 6 Technology Park Drive Westford, MA 01886 USA Phone: +1 978 577 4000 Email: VideoApps@tycoint.com Web: www.illustracameras.com

ILLUSTRA PRO LT 5MP NETWORK IP INDOOR FISHEYE CAMERAS

(ADCi825LT-F311 & ADCi825LT-F312)

MasterFormat 2016:

28 21 13	IP Cameras

Notice

Please read this A&E document thoroughly and save it for future use before attempting to specify this unit. The information in this document was current when published. The manufacturer reserves the right to revise and improve its products. All specifications are therefore subject to change without notice.

Trademarks

The trademarks, logos, and service marks displayed on this document are registered in the United States [or other countries]. Any misuse of the trademarks is strictly prohibited and Tyco Security Products will aggressively enforce its intellectual property rights to the fullest extent of the law, including pursuit of criminal prosecution wherever necessary. All trademarks not owned by Tyco Security Products are the property of their respective owners, and are used with permission or allowed under applicable laws.

| Illustra Pro 5MP Fisheye Model Description | Product Codes |
| --- | --- |
| Illustra Pro LT 5MP Fisheye, indoor, white, vandal | ADCi825LT-F311 |
| Illustra Pro LT 5MP Fisheye, indoor, white, non-vandal | ADCi825LT-F312 |

# Description

The Illustra Pro LT 5MP Fisheye Camera (hereafter referred to as the camera) operates across an IP network, e.g. the Internet, a LAN or WAN. The video output from the camera is compressed and sent across the network using IP transport mechanisms allows complete functionality at a remote location connected by any kind of IP network. A built-in web server provides web pages to configure the dome and streams the video using a customer-selected set of protocols with a standardized transport stream. This will also support other metadata as required. Emails and movie clips (AVI) may be sent across the network in response to alarms. The Camera can operate as a standalone camera on a network however it is intended to be integrated into sophisticated security solutions.

The Camera   can network with network video recording systems using Illustra API v3.0. These systems include American Dynamics victor Unified Client, American Dynamics VideoEdge NVR, ExacqVision NVR.

The Camera is a Network Video Transmitter, NVT, compliant with ONVIF 2.4 profile S standards, and can interface with network video clients supporting ONVIF.

The Camera is compatible with the American Dynamics Illustra Connect tool which provides discovery, configuration, firmware upgrade and diagnostics using ONVIF and WS Discovery protocols.

Sleek, discreet design allows it to blend into any environment for inconspicuous surveillance.

The vandal-resistant model protects the camera against external impacts.

The Pro LT 5MP Fisheye cameras include a mounting adaptor for installations using standard single-gang and double-gang electrical boxes.

For pendent installation, the Pro LT 5MP Fisheye cameras can be used with the Illustra 600 Series White Outdoor Pendent Cap (ADCI6DPCAPOW).

It is extremely easy to install and simple to set up.

A built-in web server provides easy configuration.

Key differentiators are:

- 5MP imager for super high quality images with fisheye resolution up to 1936x1936 or 3.7MP

- Efficient bandwidth and video storage to reduce costs

- Onboard SD card recording and storage

- Sleek, discreet design

- Quick and easy installation

- Vandal-resistant model available

- ONVIF 2.4 profile S compliant

- Low Latency

- Progressive scan imager with full digital path to output

Performance Specifications

The Camera supports Ethernet 100/100 Base-T via a RJ45 connection with support for HTTP, TCP/IP, RTP, RTSP, DHCP, multicast, and DDNS client protocols.

The Camera E supports live video via the web pages using Internet Explorer 9 or higher, Firefox or Chrome or proprietary client software.

The Camera has a 1.27mm, IR Corrected lens delivering a 183° Field of View (FOV)

The Camera uses DNS protocol to resolve network names and also DDNS Dynamic Domain Name System for updating, in real time, a changing IP address on the Internet to provide a persistent domain name for a resource that may change location on the network per RFC 2136 Dynamic Updates in the Domain Name System.

The Camera supports NTP for time synchronization.

The Camera is able to send email alerts via SMTP to one specified mailbox using a specified SMTP server. The product supports basic authenticated SMTP using username and password for login on the SMTP server.

The product supports WS-Discovery for discovery purpose.

The Camera interfaces with the Illustra Connect application to provide a robust tool for discovery, snapshot, configuration, diagnostics, and firmware upgrade; the following is provided:

- As an alternate to the list display a snapshot view of all cameras can be displayed.

- Device properties windows can be opened to show a snapshot of the camera view, network settings, UUID (ONVID identification code), serial number, and many other device properties.

- Support of IPv4 and IPv6 together or separately with user choice preference for dual stack devices.

- Resolve IP address conflicts and configure devices with static IP addressed or DHCP

- Configure individual device network setting.

- Provides a device list in exportable CVS format

- User account control to secure full administrator access

- Device maintenance allows individual device configuration

- Device maintenance allows three types of reset/reboot:

  - Reset to factory defaults and change IP settings

  - Reset to factory defaults and preserve IP settings

  - Reboot maintaining current settings

  - Multiple devices can be updated with one operation for the following:

    - Time

    - Date

    - NTP server

    - Upgrade firmware

    - User accounts

    - Network settings

- Provided as a virtualized standalone .exe file that does not require PC installation. This self-contained version of Illustra Connect can run with no prerequisites, and can also be used from a USB flash drive.

- The Illustra Connect tool is also available as an installation setup file which will be able to store any user specified detail such as security settings and network preferences for future use.

- Both the virtualized and installation files of Illustra Connect are available for download from the American Dynamics website.

- Supports all the language options of the camera

The following information is available for display in the Camera GUI:

- Camera Name

- Model

- Product Code

- Manufacturing Date

- Serial Number

- MAC Address

- Firmware Version

- Hardware Version

The System Log is available for display in the GUI, this provides the most recent system messages and the information will include the following:

- Messages about system behavior such as process startup/shutdown.

- Warnings about recoverable problems that processes encounter.

- Error messages where processes encounter problems they cannot fix, even if it can continue to work.

The Camera provides a Boot log, which is a log of the Linux operating system boot processes and is useful to American Dynamics support engineers who require additional information on the device.

Minimum Performance Specifications

| Camera |  |
| --- | --- |
| Video Compression | H.264/MJPEG |
| Max Frame Rate | 14ips |
| Stream | Dual |
| ONVIF Compliant | Yes |
| Imager | Type 1/2.5” 5MP CMOS Sensor |
| Minimum Illumination | 1.2 lux |
| Shutter | AES (Automatic Electronic Shutter) |
| Lens Focal Length | 1.37mm |
| Aperture | 2.0 |
| Field of View | 183° |
| PTZ | No |
| White Balance | Auto Normal, Auto Wide and Manual |
| Alarms | Motion detection |
| Wide Dynamic Range | 82dB |
| Privacy Zones | Yes, 4 |
| Menu Languages | English (default), Arabic, Czech, Danish, German, Spanish, French, Hungarian, Italian, Korean, Japanese, Netherlands, Polish, Portuguese, Swedish, Turkish, Chinese Traditional, Chinese Simplified |
| Resolutions |  |
| Fisheye Stream 1 | 1936x1936 |
| Fisheye Stream 2 | 736x736 |
|  | 640x640 |
|  | 320x320 |
|  | 176x176 |
| Network |  |
| Ethernet | 10/100Base-T |
| Supported Protocols | TCP/IP, IPv4, IPv6, TCP, UDP, HTTP, FTP, DHCP, WS-Discovery, DNS, DDNS, RTP, TLS, Unicast, Multicast, NTP, SMTP, WS-Security |
| Base Protocol | TCP/IP - RFC4614 |
| Internet Layer Addressing | IPv4 - RFC791 |
|  | IPv6 - RFC2460 |
| Transport Layer | TCP - RFC973 |
|  | UDP - RFC768 |
| Data Transmission | HTTP - RFC2616 |
|  | FTP - RFC959 |
| Network Address Configuration | DHCP - RFC2131 |
|  | Zeroconf - RFC3927 |
|  | Static IP address |
| Network Name Resolution | DNS - RFC5395 |
|  | DDNS - RFC 2136 |
| Time Synchronization | NTP - RFC1305 |
|  | IETF NTP Working Group |
|  | 1 minute poll rate |
| Email | SMTP - RFC5321 |
|  | Authenticated SMTP - RFC4954 |
| Authentication and Security | TLS - RFC5346 |
|  | HTTPS (HTTP over TLS) - RFC2818 |
|  | WS-Security |
| Discovery | WS-discovery - ws-discovery.pdf |
| Streaming | RTP - RFC3550 |
|  | RTSP - RFC2326 |
|  | Unicast Streaming |
|  | Multicast Streaming - RFC1112 level 1 |
| External Interface Protocol | AD Illustra API 3.0 |
|  | SOAP - SOAP 1.2 |
|  | ONVIF |
|  | WS-Addressing |
|  | WS-Eventing |
| Onboard Storage |  |
| Card Type | 32 GB Micro SDHC |
| Electrical |  |
| Power | PoE 802.3af Class 3 |
| Power Consumption | <12.95W |
| Surge Protection | Data lines isolation transformer coupled |
| Connectors | RJ-45 for 10 BaseT/100BaseTX |
| Physical |  |
| Body Diameter | 149mm (5.85in) |
| Height Above Ceiling | 25.4mm (1.0in required for cable clearance) |
| Height Below Ceiling | Vandal-Resistant | 60mm (2.36in) |
|  | Non Vandal-Resistant | 74mm (2.91in) |
| Weight | Vandal-Resistant | 0.750 kg |
|  | Non Vandal-Resistant | 0.730 kg |
| Environmental |  |
| Operating Temperature | -10°C to 45°C (14°F to 113°F) |
| Humidity | 95% non-condensing |
| Storage Temperature | -20°C to 65°C (-4°F to 149°F) |
| Regulatory |  |
| Emissions | FCC CFR 47 Part 15 Class A |
|  | AS/NZS CISPR22 Class A |
|  | ICES-003/NMB-003 Class A |
|  | EN 55022 |
| Immunity | EN50130-4 |
|  | EN 61000-6-1 |
|  | IEC 62599-2 |
|  | EN 55024 |
| Safety | UL 60950-1 |
|  | CSA 22.2 No. 60950 |
|  | EN 60950-1 |
|  | IEC 60950-1 |
| Environmental | RoHS, EU Directive 2002/95/EC |
|  | WEEE, EU Directive 2002/96/EC |
| Physical Protection | IK10 |

# Text boxes

Non Vandal-Resistant

Vandal-Resistant